## Slide 1: POWER MANAGEMENT IN ARDUINO

## Slide 2: Power supply for Arduino Projects
Power Supply for Arduino Projects can range from USB power which is the simplest and most common, DC barrel jacks for higher amounts of power supply to the VIN pins similar to the barrel jacks and 5V pin which bypasses the on board voltage regulators.
Batteries used in the power supply systems can be 9V, Lithium polymer, AA or AAA batteries.

## Slide 3: Current requirements and draw for different boards and components
Boards
Arduino Uno- Recommended input is 7-12 V. Operating voltage is 5V. Maximum input voltage is 20V. Current Draw is 50mA.
Arduino Due- Recommended input is 7-12 V. Operating voltage is 3.3V. Maximum input voltage is 15V. Current Draw is 50mA.
Arduino MKR Series-Recommended input is 5V. Operating voltage is 3.3V. Maximum input voltage is 6V. Current Draw is 20mA.
Arduino Pro Mini-Recommended input is 7-12 V. Operating voltage is 5V. Maximum input voltage is 12V. Current Draw is 20mA.
Note: Arduino Nano, Mega 2560 and Leonardo have similar specifications to the Arduino Uno all that differs is the current draw.

## Slide 4: Current requirements and draw for different boards and components(contd.)
Peripherals
Sensors- Operating Voltage is 3.3V or 5V depending on the sensor. During measurement the current draw of DHT11 is 2.5mA and BMP180 is 3mA.
Displays- Operating voltage of LCDs and OLED is 3.3-5V and the current draw is 20mA for LCD and 20-100mA for OLED. Regular LEDs have a forward voltage of 2-3.3V and current draw of 20mA.
Actuators- Operate between 12 and 24V depending on the application with a current draw of 40mA that may vary depending on the load.
User inputs- Operating voltage of 0-5V or 0-3.3V depending on the board with a current draw so low it is negligible.